# Van’s Aircraft

# RV-9

# Lycoming O-290-D2

# Pilot’s Operating Handbook

N941WR

PERFORMANCE – SPECIFICATIONS

SPAN	………………………………………………………….	28’ 0”

LENGTH	………………………………………………………	20’ 5”

HEIGHT	……………………………………………………….	6’ 0”

SPEED:

Maximum at Sea Level	………………………………………..	180 MPH

Cruise, 75% Power at 8,000 Ft	  …………….…………………..	175 MPH

RANGE (includes 3 gal. for taxi, takeoff & climb):

75% @ 8000’ , no reserve	.……..… ………………………….	745 sm

55% @ 8000’  no reserve	…………….……………………….	910 sm

75% @ 8000’, one hour (8 gal) reserve	………………………	570 sm

55% @ 8000’, one hour (8 gal) reserve	………………………	750 sm

RATE OF CLIMB AT SEA LEVEL	…………………………	1,150 FPM

SERVICE CEILING	……………….……………………….….	19,000 FT

TAKEOFF PERFORMANCE	…………………………….…...	500 Ft

LANDING PERFORMANCE	 ... …………………….…………	410 Ft

STALL SPEED (CAS):

Flaps Up, Power Off.………………..………………	49 MPH

Flaps Down, Power Off.…………..…………………	44 MPH

MAXIMUM WEIGHT (Normal Category)	……………………	1750 Lbs

EMPTY WEIGHT	……………………………………………	1040 Lbs

MAXIMUM USEFUL LOAD	 ...………………………………	710 Lbs

BAGGAGE ALLOWANCE	…………………………………	100 Lbs

WING LOADING (Pounds/ Sq. Ft)	…………………………	14.1 lb/sqft

POWER LOADING (Pounds/ HP)	……………………………	12.5 lb/hp

FUEL: Capacity	……………………………………………	36 Gal Total

Type:	……………………………………………	80 / 100LL Avgas

Or

Auto fuel - 80 Octane Minimum

OIL CAPACITY	……………………………………………...	8 Qts max

ENGINE	…………………….…………………….	Lycoming O-290-D2

HORSEPOWER 	…………………………	140 HP @ 2800 RPM / 5 Min

135 HP @ 2600 RPM Continuous

PROPELLER	………….…………	Catto 2-Blade wood/glass composite

68” diameter x 64” pitch

Performance

| TAS | RPM | MAP | HP | Fuel Flow GPH | % Power |
| --- | --- | --- | --- | --- | --- |
|  | 2800 | “ | 140 | --- | Takeoff |
| 180 | 2600 | “ | 135 | 12.6 | 100 |
| 175 | 2350 | “ | 101 | 7.2 | 75 |
| 165 | 2200 | “ | 87 | 6.3 | 65 |
| 157 | 1860 | “ | 74 | 5.3 | 55 |

Fuel flow are based on Peak CHT enriched by 50 degrees.

No Wind Range at 8,000’:

- All range calculations include 3 gal. for engine start, taxi, takeoff and climb.

- Engine is leaned for best economy.

One hour (7.2 gal.) reserve:

75% Power	………………………………………	570 sm

65% Power	………………………………………..		660 sm

55% Power	………………………………………..	750 sm

No Reserve:

75% Power ………………………………………..	745 sm

65% Power ………………………………………..	827 sm

55% Power ………………………………………..	910 sm

AIRSPEED LIMITATIONS

|  | SPEED | IAS | REMARKS |
| --- | --- | --- | --- |
| VNE | Never Exceed Speed | 210 mph | Do not exceed this speed in any operations. |
| VNO | Maximum Structural Cruising Speed | 180 mph | Exceed this speed only in smooth air. |
| VA | Maneuvering Speed | 118 mph | Do not make full control movements above this speed. Full elevator deflection will result in a 6g load at this speed. |
| VFE | Maximum Flap Extended Speed | 90 mph | Do not exceed this speed with flaps down |
| Vy | Best Rate of Climb | 86 mph |  |
| Vx | Best Angle of Climb | 74 mph |  |
| Vs | Stall Speed Clean | 49 mph |  |
| Vso | Stall Speed Landing Configuration | 44 mph |  |

AIRSPEED INDICATOR MARKINGS

| MARKING | IAS VALUE OR RANGE | SIGNIFICANCE |
| --- | --- | --- |
| White Arc | 49 – 90 mph | Full Flap Operating Range. Lower limit is Vso. Upper limit is maximum speed with flaps extended |
| Green Arc | 56 – 180 mph | Normal Operating Range. Lower limit is Vs. Upper limit is maximum structural cruising speed |
| Yellow Arc | 180 – 209 mph | Operations must be conducted with caution and only in smooth air. |
| Blue Line | 118 | Maneuvering speed – Max. permissible speed at which full control can be applied. |
| Red Line | 210 mph | Maximum speed for all operations |

WEIGHT AND BALANCE DATA

Make:  William Repucci	Model:  RV-9

Serial #:  90737	Registration:  N941WR

MAXIMUM WEIGHTS AND LIMITS:

Aerobatic Category	…………………	Not approved for Aerobatics

Utility Category	…………………………………….	1600 Lbs

Normal Category	…………………………………	1750 Lbs

Forward CG Limit	…………………………………	15% of chord

7.95” aft of leading edge

Aft CG Limit	………………………………………	28% of chord or

14.84” aft of leading edge

Utility Aft CG Limit	………………………………	24% of Chord or

12.72” aft of leading edge

Datum:	…………………	70 inches forward of wing leading edge (L.E.)

Design C.G. Range:	…………………………	15% to 28% of wing chord

7.95” to 14.84” from L.E

.	77.95” to 84.84” aft of Datum

Wing L.E.:	…………………………………	70 inches aft of datum

Main wheel right:	…………………………	 68.75” aft of datum

Main wheel left:	…………………………	68.75” aft of datum

Tail wheel:	…………………………………	244.75” aft of datum

Fuel:	………………………………………	76.75” aft of datum

Pilot and Passenger:	………………………	92.7” aft of datum

Baggage:	……………………………………	122” aft of datum

Aircraft weighed empty in level flight attitude. (Includes 8 qts. of oil, unusable fuel)

Weight		Arm		Moment

Right Wheel	467	68.62	34106.8

Left Wheel	 466	68.75	34787.5

Tail Wheel	57	24.75	13216.5

Total		990		65493.8

Empty CG = 79.06” aft of datum

WEIGHT AND BALANCE DATA

Sample:

Weight	Arm	Moment

Aircraft	990	78.82	78021.8

Fuel (6lbs/gal)			76.75

Pilot			92.70

Passenger			92.70

Baggage			122.00

Total

CG = Total Moment / Total Weight

CG = 		 in aft of datum

CG Range = 77.95 to 84.84 in aft of datum

##### WEIGHT AND BALANCE DATA

# PREFLIGHT INSPECTION

1. CABIN

- Documentation – Available In Airplane

- Aeronautical Charts – CURRENT AND APPROPRIATE TO FLIGHT

- Flight Control Locks – RELEASE

- Ignition Switches – OFF

- Avionics Switch – OFF

- Master Switch – ON

WARNING

When turning on the master switch, using an external power source, or pulling the propeller through by hand, treat the propeller as if the ignition switches were on.  Do not stand, nor allow anyone else to stand, within the arc of the propeller, since a loose or broken wire, or a component malfunction, could cause the propeller to rotate.

- Fuel Quantity – CHECK QUANTITY – VERIFY ENGINE MONITOR RESET

- Fuel Shutoff Valve – Left Tank

- Fuel Pump – ON – VERIFY FUEL PRESSURE

- Fuel Pump – OFF

- Flaps – DOWN

- Navigation, Strobe, and Landing light functionality - Verify

- Master Switch – OFF

2. STATIC PORT

- Static Sources – CHECK for blockage

3. EMPENNAGE

- Tail Tie-Down – DISCONNECT

- Tail Wheel – Check condition and Springs

- Control Surfaces – CHECK freedom of movement and security

4. STATIC PORT

- Static Sources – CHECK for blockage

5. FLAPS

- Flap – CHECK security and travel

6. AILERON

- Aileron  – CHECK freedom of movement and security

7. RIGHT WING TIP

- Navigation and Strobe Light – CHECK condition

- Landing Light – CHECK condition

8. RIGHT WING

- Wing Tie-Down – DISCONNECT

- Fuel Quantity – CHECK VISUALLY

- Fuel Filler Cap – SECURE

- Main Wheel Tire – CHECK for proper inflation

- Chock – REMOVE

- Right Wing Tank – SUMP

9. NOSE

- Engine Oil Level – CHECK, do not operate with less than 5 quarts

- Gascolator – SUMP

- Propeller and Spinner – CHECK for nicks and security

- Cowl Camlocks – CHECK for security

- Air Inlet – CHECK for restrictions

- Fuel Tank Vents – CHECK for blockage

10. LEFT WING

- Main Wheel Tire – CHECK for proper inflation

- Chock – REMOVE

- Left Wing Tank – SUMP

- Fuel Quantity – CHECK VISUALLY

- Fuel Filler Cap – SECURE

- Pitot Tube Cover – REMOVE and check for blockage

- Wing Tie-Down – DISCONNECT

11. LEFT WING TIP

- Landing Light – CHECK condition

- Navigation and Strobe Light – CHECK condition

12. AILERON

- Aileron  – CHECK freedom of movement and security

13. FLAPS

- Flap – CHECK security and travel

#### BEFORE STARTING ENGINE

- Preflight Inspection – COMPLETE

- Seat Belts and Shoulder Harnesses – ADJUST and LOCK

- Canopy – Open or Closed depending on weather

- Fuel Selector Valve – LEFT TANK

- Master Switch – Off

- Avionics Master – OFF

- Brakes – SET

### STARTING ENGINE (COLD)

- Master Switch – ON

- Strobe – ON

- Flaps – UP

- Carb Heat – COLD

- Throttle – OPEN 1/4

- Mixture – FULL RICH

- Fuel Pump – ON

- Pump throttle to full open and back to idle – 1 to 2 strokes

- Propeller Area – CLEAR

- Ignition Switches – ON Aircraft Power

- Starter Button – PRESS

- Throttle – ADJUST to 1000 rpm

- Oil Pressure – CHECK   25 psi at idle

- Alternator – ON

- Avionics – ON

### STARTING ENGINE (HOT)

- Master Switch – ON

- Strobes – ON

- Flaps – UP

- Boost Pump – ON

- Mixture – FULL AFT

- Throttle – FULL FORWARD

- Mixture – OPEN momentarily to clear any bubbles then CLOSE

- Mixture – OPEN momentarily to prime then FULL AFT

- Throttle – CLOSE then OPEN 1/4

- Propeller Area – CLEAR

- Ignition Switches – ON

- Starter Button – PRESS

- Mixture – FORWARD once engine starts

- Oil Pressure – CHECK   25 PSI at idle

- Alternator – ON

- Avionics – ON

TAXIING

When taxiing, it is important that speed and use of brakes be held to a minimum and that all controls be utilized (see Taxiing Diagram) to maintain directional control.

The carburetor heat control knob should be pushed full in during all ground operations unless heat is absolutely necessary.

Taxiing over loose gravel or cinders should be done at low engine speed to avoid abrasion and stone damage to the propeller tips.

BEFORE TAKEOFF

- Brakes – SET

- Flight Controls – FREE and CORRECT

- Flight Instruments – SET

- Altimeter and EFIS – CORRECT BARO PRESSURE

- Fuel Selector Valve – DESIRED TANK

- Elevator and Aileron Trim – NEUTRAL

- Throttle – 1800 RPM

- Carb Heat – Check

- Left Magneto – Check Ship Power  (may be no RPM drop)

- Left Magneto – Check Self Power  (may be no RPM drop)

- Right Magneto – Check Ship Power  (may be no RPM drop)

- Right Magneto – Check Self Power  (may be no RPM drop)

- Engine Instruments – CHECK

- Throttle – Full Power – Check for engine roughness

- Throttle – IDLE

- Radios – SET

- Transponder – ALT

- Check Flight Timer in EFIS

- Canopy  -------- Overhead Latch – SECURE

- Canopy  -------- Side Latch – SECURE

TAKEOFF

#### NORMAL TAKEOFF

- Wing Flaps – UP

- Throttle – FULL FORWARD

- Elevator Control – LIFT TAIL WHEEL (at 55 IAS)

- Climb Speed – 110 IAS

#### SHORT FIELD TAKEOFF

- Wing Flaps – 10 Deg

- Brakes – APPLY

- Throttle – FULL FORWARD

- Stick  – FULL BACK

- Brakes – RELEASE

- Climb Speed – 80 IAS (Vy)

##### ENROUTE CLIMB

- Airspeed – 110 - 130 IAS

- Throttle – 25 in Hg, or full throttle

- Prop – 2500 RPM

- Fuel Pressure – CHECK

##### CRUISE

##### (65% Power)

- Throttle – 23 in Hg

- Prop – 2300 RPM

- Trim – ADJUST

- Mixture – Adjust as necessary

##### LANDING

- Fuel Selector – To fullest tank

- Slow to 90 IAS

- Flaps – as needed below 90 MPH

- Mixture – Full rich

- Fuel pump – On

- Landing Lights – as needed

##### POST FLIGHT

##### AFTER LANDING

- Wing Flaps – DOWN

- Transponder – STANDBY

- Carb Heat – Cold

ENGINE SHUTDOWN

- Throttle – IDLE  (800 to 900 RPM until drop in Cylinder Head Temperature)

- Avionics Master – OFF

- Fuel Pump – OFF

- Fuel Selector Valve – OFF

- Mixture – FULL AFT

- Ignition Switches – OFF

- Strobe – OFF

- Flaps – DOWN

- Alternator – OFF

- Master Switch – OFF

#### SECURING AIRCRAFT

- Wheel Chocks – INSTALL

- Wing & Tail Tie-Down – INSTALL AS REQUIRED

- Pitot Tube Cover – INSTALL AS REQUIRED

- Cockpit – CLEAN AND SECURE CONTROLS

- Master and Electrical Switches – OFF

- Engine Monitor Fuel Quantity – RESET AFTER REFUELING

Engine Information

Model: ……..	Lycoming O290-D2

HP: …………	140 – 5 min / 135 – Continuous

Fuel: ………..	80, 100 LL, or 86 Octane auto fuel

Oil Filter: …..	Champion CH48108-1

OIL:	Phillips 20W50

Average		MIL-L-22851

Ambient Air	MIL-L-6082 	Ashless Dispersant

All Temperatures	------	SAE 15W50 or 20W50

Above 80 o F	SAE 60	SAE 60

Above 60 o F	SAE 50	SAE 40 or SAE 50

30 o F to 90 o F	SAE 40	SAE 40

0 o F to 70 o F	SAE 30	SAE 40, 30 or 20W40

Below 10o F	SAE 20	SAE 30 or 20W30

###### Oil Sump Capacity …….. 8 U.S. Quarts

###### Minimum Safe Quantity ...2 U.S. Quarts

###### Operating Conditions:

###### Oil Inlet Temp:	180o F desired

###### 245o F Maximum

###### Oil Pressure:	90 psi max

###### 60 psi min

###### 25 psi idle

###### Fuel Pressure:	8 psi max

3 psi desired

.5 psi min

CHT:	500o F Maximum

150 to 435o F for continuous operation

###### EMERGENCY OPERATIONS

###### AIRSPEEDS

Engine Failure After Takeoff:

Wing Flaps Up	…………………………………………	80 IAS

Wing Flaps Down	……………………………………..	70 IAS

Maneuvering Speed (Va)	……………………………………….	118 IAS

Maximum Glide	………………………………………………… 	80 IAS

ENGINE FAILURES

ENGINE FAILURE DURING TAKEOFF RUN

- Throttle –IDLE

- Brakes – APPLY

- Wing Flaps – RETRACT

- Ignition Switches – OFF

- Master Switch – OFF

ENGINE FAILURE IMMEDIATELY AFTER TAKEOFF

- Airspeed – 70 IAS

- Mixture – IDLE CUT-OFF

- Fuel Selector Valve – OFF

- Ignition Switches – OFF

- Wing Flaps – AS REQUIRED

- Master Switch – OFF

ENGINE FAILURE DURING FLIGHT

- Airspeed –70 IAS

- Carburetor Heat – ON

- Fuel Pump – ON

- Mixture – RICH

- Fuel Selector – SWITCH TANK

- Ignition Switches – ON

- Attempt restart

- Transponder – 7700

###### EMERGENCY OPERATIONS

###### LANDING

EMERGENCY LANDING

- AVIATE – NAVIGATE – COMMUNICATE

- Airspeed – 70 IAS

- Select suitable landing spot and turn to it

- Harness – SECURE

- Fuel Pump – OFF

- COMMUNICATE – SOS 129.1

- Fuel Selector – OFF

- Transponder – 7700

- Canopy – Unlatch overhead and side releases

- Flaps – As needed

- Master – OFF

- Touch down at minimum controllable airspeed

###### DITCHING (WATER LANDING)

EMERGENCY WATER LANDING

- AVIATE – NAVIGATE – COMMUNICATE

- Airspeed – 70 IAS

- Select suitable landing spot close to shore, if possible.

- APPROACH – High Winds, Heavy Seas – INTO THE WIND

– Light Winds, Heavy Swells – PARALLEL TO SWELLS

- COMMUNICATE – TRANSMIT MAYDAY on 121.5

- Transponder – 7700

- Canopy – Unlatch overhead and side releases

- Harness – SECURE (Brief passenger on Release Mechanism.)

- Heavy Objects – SECURE (Remove object from glare shield.)

- Fuel Pump – OFF

- Fuel Selector – OFF

- Flaps – FULL

- Touch down – 2 MPH above stall speed

- Face – CUSHION at touchdown with folded coat

- Airplane – EVACUATE

- Life Vests and Raft - INFLATE

###### EMERGENCY OPERATIONS

FIRES

DURING START ON GROUND

- Cranking – CONTINUE, to get a start which would suck the flames and accumulated fuel through the servo and into the engine.

If engine starts:

- Power – 1700 RPM for a few minutes

- Engine – SHUTDOWN and inspect for damage

If engine fails to start:

- Throttle – FULL OPEN

- Cranking – CONTINUE

- Fire Extinguisher – OBTAIN

- Engine – SECURE

ENGINE FIRE IN FLIGHT

- Fuel Selector Valve – OFF

- Master Switch – OFF

- Cabin Heat and Air – OFF

ELECTRICAL FIRE IN FLIGHT

- Master Switch – OFF

- Avionics – OFF

- All Other Switches (except magneto) – OFF

- Vents/ Cabin Air/ Heat – CLOSED

- Fire Extinguisher – ACTIVATE (if available)

CABIN FIRE

- Master Switch – OFF

- Vents/ Cabin Heat – CLOSED

- Fire Extinguisher – ACTIVATE (if available)

###### EMERGENCY OPERATIONS

FIRES - continued

WING FIRE

- Nav & Strobe Lights – OFF

- Landing Lights – OFF

ELECTRICAL

ELECTRICAL / ALTERNATOR FAILURE

- Avionics –OFF

- Alternator Switch – OFF

- Alternator Switch – ON

IF ALTERNATOR IS STILL OFF-LINE:

- Alternator Switch – OFF

- Electrical Switches – OFF except Ignition

- Avionics – OFF

- Avionics – ON as required

- Electrical Equipment – ON, as required

- Flight – TERMINATE as soon as practical.