# Van’s Aircraft RV-9

# Condition Inspection Checklist

N941WR

HOURS

Engine:

Airframe:

MAKE:	RV-9

SERIAL #:	90737

REGISTRATION #:	N941WR

DATE:

PERFORMED BY:

(Print Name)

(Signature)

REPAIRMAN’S CERTIFICATE NUMBER:

CONSUMABLES

    - Oil – 8 Quarts

OIL: Phillips 20W50

Average		MIL-L-22851

Ambient Air	MIL-L-6082 	Ashless Dispersant

All Temperatures	------	SAE 15W50 or 20W50

Above 80 o F	SAE 60	SAE 60

Above 60 o F	SAE 50	SAE 40 or SAE 50

30 o F to 90 o F	SAE 40	SAE 40

0 o F to 70 o F	SAE 30	SAE 40, 30 or 20W40

Below 10o F	SAE 20	SAE 30 or 20W30

    - Oil Filter: Champion CH48108-1

    - Lubricants ???

Wheel bearing grease: Hi-temp disc brake grease or Aeroshell 5

Gasket lube: Dow DC-4

Light lubricant: LPS-2 or comparable light lubricant for rod end bearings

    - Brake Pads ???

    - Tires

Main Tire Size:  2 - 5:00x5-6 ply, as needed

Tail Wheel Size

    - Spark Plugs

Type: NGK BR8ES

Gap: ???

    - ELT Batteries (8 - Duracell MN1300 alkaline D-cell (every 2 years))

    - ELT Remote Battery (1 - Duracell DL 1/3 NB lithium (every 8 years))

    - Air filter recharge kit (K&N 99-5000)

    - Alternator belt  (NAPA part number: 4L310W, ½ x 31” or 12.5/13mm x 785 mm)

TIME-LIMITED ITEMS

| Item | Last change | Next due |
| --- | --- | --- |
| ELT batteries (replace every 2 years) |  |  |
| ELT remote battery (replace every 8 years) |  |  |
| Altitude encoder & transponder certification |  |  |

PROPELLER GROUP

    - Remove spinner, noting orientation for reinstallation

    - Inspect spinner and back plate

    - Inspect blades for nicks and cracks

    - Check for grease and oil leaks

    - Check spinner mounting brackets

    - Inspect hub parts for cracks and corrosion.

    - Remove safety wire, inspect prop bolts and nuts.

    - Re-torque prop bolts to 35 ft-lbs

    - Install safety wire or cotter pins on prop bolts

    - Re-install spinner

ENGINE GROUP

    - Remove engine cowl

    - Clean and check cowling for cracks, distortion and loose or missing fasteners

    - Drain oil sump, collect oil sample for analysis

    - Re-install / close oil drain

    - Fill engine with oil per lubrication chart

    - Check oil with magnet for ferrous metal

    - Remove, inspect, and replace oil filter and torque to 16 – 20 ft-lbs

    - Install oil filter safety wire

    - Cut open oil filter – inspect for contamination

    - Check oil temp. sender for leaks and security

    - Check oil lines and fittings for leaks, chafing security, dents and cracks

    - Check battery boxes, batteries and cables

    - Clean and check oil cooler fins

    - Clean engine

    - Remove all spark plugs, noting location

    - Check condition of spark plugs, adjust gap

Firing order: 1 – 3 – 2 – 4

    - Install lower spark plugs w/ anti-seize paste – Torque to ???

    - Check ignition harness and insulators.

    - Conduct a compression check

#1 ____/80,  #2 ____/80,

#3 ____/80,  #4  ____/80

    - Install upper spark plugs w/ anti-seize paste – Torque to ???

    - Check magneto timing (18o BTC)

    - Remove air filter and clean

    - Check intake seal for leaks and clamps for tightness

    - Clean screens in gascolator

    - Inspect condition of fuel lines

    - Check fuel system for leaks

    - Check throttle body attaching screws – 40 to 50 in - lbs

    - Check engine control – Throttle

    - Check engine control – Mixture

    - Check engine control – Carb Heat

    - Inspect exhaust stacks, connections, gaskets

    - Re-torque exhaust mounting nuts – 160 to 180 in-lbs

    - Inspect heat exchange and baffles

    - Check breather tube for obstructions and security

    - Check crankcase for cracks, leaks, security of bolts

    - Check engine mounts for cracks and loose mountings

    - Check firewall seals

    - Check condition and tension of alternator and drive belt

    - Check condition of starter

    - Check fluid in brake reservoir

    - Lubricate all controls

    - Reinstall engine cowl

CABIN GROUP

    - Inspect canopy and windows

    - Check   upholstery for tears

    - Check seats, seat belts, shoulder straps

    - Check trim operation

    - Check rudder pedals

    - Check electric fuel pump for operation

###### Fuel Pressure:	8 psi max

3 psi desired

.5 psi min

    - Check control column, systems and connection

    - Check landing, nav, cabin, and instrument lights

    - Check instruments, lines and attachments.

    - Check operation ofx fuel selector valve

    - Check condition of heater controls

    - Check condition and operation air vents

FUSELAGE AND EMPENNAGE GROUP

    - Remove inspection plates and panels

    - Check electronic installations

    - Check bulkheads and stringers for damage

    - Check antenna mounts and wiring

    - Check fuel lines and valves

    - Check vertical fin and rudder surfaces

    - Check rudder horn and attachment

    - Check vertical fin attachments

    - Check rudder bolts for wear

    - Check horizontal stabilizer and elevators

    - Check horizontal stabilizer attachment

    - Check elevator trim servo for wear and operation

    - Check elevator horn

    - Check elevator bolts for wear

    - Check elevator bell cranks and controls.

    - Lubricate all bearings as needed

    - Reinstall inspection plates and panels

WING GROUP

    - Remove inspection plates

    - Check surfaces and tip for damage and loose rivets and condition of walkways

    - Check aileron mounts and attachments

    - Check aileron bellcrank and control tubes

    - Check flaps and attachment for damages

    - Check all wing attachment bolts

    - Check fuel tanks and lines for leaks

    - Check fuel tank vents

    - Reinstall inspection plates

LANDING GEAR GROUP

Main Wheels

    - Check main gear attachments

    - Check tires for cuts and wear

    - Remove main wheels, clean, and repack bearings

    - Check wheels for cracks, corrosion and broken bolts

    - Check tire pressure (32 PSI)

    - Check brake lining and disc

(Min disc thickness: 0.167”.  Groves no deeper than 0.030”)

    - Check brake lines

Tail Wheel

    - Remove, inspect, clean, grease, and reinstall

    - Inspect springs

    - Inspect spring attach points for excess wear.  Repair, if needed.

OPERATIONAL INSPECTION

    - Check fuel pump and fuel tank selector

    - Check fuel pressure

    - Check oil pressure and temperature

    - Check alternator output

    - Check manifold pressure

    - Check Cabin heat operation

    - Check throttle and mixture operation

    - Check propeller smoothness

    - Check electronic equipment operation

KNOWN PROBLEM AREAS:

    - Smoking rivets on forward bottom skin

    - Chafing brake lines on gear leg fairing and beneath wheel pant

    - Chaffing of wheel on wheel pant

    - Fretting corrosion at gear leg fairing intersection

    - Corrosion of exposed rod end bearings

    - Rudder contacting elevator roots in flight (dynamic clearance less than static clearance!)

LOG BOOKS:

    - Sign and date Airframe log

    - Sign and date Engine log

    - Sign and date Propeller log

NOTES:

##### Engine Information

Model: ……..	Lycoming O290-D2

HP: …………	140 – 5 min / 135  - Continuous

Fuel: ………..	80, 100 LL, or 86 Octane auto fuel

Oil Filter: …..	Champion CH48108-1

OIL: Phillips 20W50